## Slide 1
Linux Ethernet Driver

## Slide 2
Contents
1. Introduction
2. Overview of network driver flow path
3. Data structures required to write network driver
4. Understand network driver step-by-step process
Platform Ethernet driver
https://elixir.bootlin.com/linux/v6.3.2/source/drivers/net/ethernet/xilinx/xilinx_axienet_main.c
PCI bus based Ethernet drivers Realtek/Intel IGB
https://elixir.bootlin.com/linux/v6.3.2/source/drivers/net/ethernet/realtek/8139cp.c
https://elixir.bootlin.com/linux/v6.3.2/source/drivers/net/ethernet/intel/igb/igb_main.c

## Slide 3
The below network driver concepts are explained with respect to RealTek 8139C+ PCI, Intel IGB driver, and Xilinx AXI platform ethernet driver(Linux Kernel version 6.0)
The high level path a packet takes from arrival to socket receive buffer is as follows:
1. Driver is loaded and initialized.
2. Packet arrives at the NIC from the network.
3. Packet is copied (via DMA) to a ring buffer in kernel memory.
4. Hardware interrupt is generated to let the system know a packet is in memory.
5. Driver calls into NAPI to start a poll loop if one was not running already.
6. ksoftirqd processes run on each CPU on the system. They are registered at boot time. The ksoftirqd processes pull packets off the ring buffer by calling the NAPI poll function that the device driver registered during initialization.
7. Memory regions in the ring buffer that have had network data written to them are unmapped.
8. Data that was DMA into memory is passed up the networking layer as an skb for more processing.
9. Incoming network data frames are distributed among multiple CPUs if packet steering is enabled or if the NIC has multiple receive queues.
10. Network data frames are handed to the protocol layers from the queues.
11. Protocol layers process data.
12. Data is added to receive buffers attached to sockets by protocol layers.
Overview of network driver flow path

## Slide 4
This entire flow will be examined in detail in the following sections.
Ethernet driver initialization and registration with PCI/Platform bus
Init_module
module_pci_driver/
pci_register_driver/
module_platform_driver
igb_probe/cp_init_one/
axienet_probe
Initialization (Init_module)
A driver registers an initialization function which is called by the kernel when the driver is loaded. This function is registered by using the module_init macro.. The igb initialization function (igb_init_module)
/**
* igb_init_module - Driver Registration Routine
*
* igb_init_module is the first routine called when the driver is
* loaded. All it does is register with the PCI subsystem.
**/
static int __init igb_init_module(void)
{
int ret;
pr_info("%s\n", igb_driver_string);
pr_info("%s\n", igb_copyright);
ret = pci_register_driver(&igb_driver);
return ret;
}
module_init(igb_init_module);
module_pci_driver(cp_driver);
static struct pci_driver cp_driver = {
.name = DRV_NAME,
.id_table = cp_pci_tbl,
.probe = cp_init_one,
.remove = cp_remove_one,
.driver.pm = &cp_pm_ops,
};
module_platform_driver(axienet_driver);

## Slide 5
PCI initialization
The Intel I350 and Realtek network cards are PCI express. PCI devices identify themselves with a series of registers in the PCI Configuration Space.
When a device driver is compiled, a macro named MODULE_DEVICE_TABLE (from include/module.h) is used to export a table of PCI device IDs identifying devices that the device driver can control. The table is also registered as part of a structure.The kernel uses this table to determine which device driver to load to control the device.Thats how the OS can figure out which devices are connected to the system and which driver should be used to talk to the device.This table and the PCI device IDs for the igb driver can be found in drivers/net/ethernet/intel/igb/igb_main.c and drivers/net/ethernet/intel/igb/e1000_hw.h, respectively: Similary PCI device id for realtek card can be found in https://elixir.bootlin.com/linux/v6.3.2/source/drivers/net/ethernet/realtek/8139cp.c
static const struct pci_device_id igb_pci_tbl[] = { { PCI_VDEVICE(INTEL, E1000_DEV_ID_I354_BACKPLANE_1GBPS) }, { PCI_VDEVICE(INTEL, E1000_DEV_ID_I354_SGMII) }, { PCI_VDEVICE(INTEL, E1000_DEV_ID_I354_BACKPLANE_2_5GBPS) }, }; MODULE_DEVICE_TABLE(pci, igb_pci_tbl); | static const struct pci_device_id cp_pci_tbl[] = { { PCI_DEVICE(PCI_VENDOR_ID_REALTEK, PCI_DEVICE_ID_REALTEK_8139), }, { PCI_DEVICE(PCI_VENDOR_ID_TTTECH, PCI_DEVICE_ID_TTTECH_MC322), }, { }, }; MODULE_DEVICE_TABLE(pci, cp_pci_tbl);
Xilinx Platform Ethernet driver, will bind according to Device tree /* Match table for of_platform binding */ static const struct of_device_id axienet_of_match[] = { { .compatible = "xlnx,axi-ethernet-1.00.a", }, { .compatible = "xlnx,axi-ethernet-1.01.a", }, { .compatible = "xlnx,axi-ethernet-2.01.a", }, {}, }; MODULE_DEVICE_TABLE(of, axienet_of_match); | 

## Slide 6
static struct pci_driver igb_driver = { .name = igb_driver_name, .id_table = igb_pci_tbl, .probe = igb_probe, .remove = igb_remove, .shutdown = igb_shutdown, .sriov_configure = igb_pci_sriov_configure, .err_handler = &igb_err_handler }; | static struct pci_driver cp_driver = { .name = DRV_NAME, .id_table = cp_pci_tbl, .probe = cp_init_one, .remove = cp_remove_one, .driver.pm = &cp_pm_ops, };
Xilinx AXI Ethernet driver probe will happen with device tree match node “.compatible” string. static struct platform_driver axienet_driver = { .probe = axienet_probe, .remove = axienet_remove, .shutdown = axienet_shutdown, .driver = { .name = "xilinx_axienet", .pm = &axienet_pm_ops, .of_match_table = axienet_of_match, }, }; | 

## Slide 7
PCI probe
Once a device has been identified by its PCI IDs, the kernel can then select the proper driver to use to control the device. Each PCI driver registers a probe function with the PCI system in the kernel. The kernel calls this function for devices which have not yet been claimed by a device driver. Once a device is claimed, other drivers will not be asked about the device. Most drivers have a lot of code that runs to get the device ready for use. The exact things done vary from driver to driver.Some typical operations to perform include:
1. Enabling the PCI device.
2. Requesting memory ranges and IO ports.
3. Setting the DMA mask.
4. The ethtool functions the driver supports are registered.
5. Any watchdog tasks needed (for example, e1000e has a watchdog task to check if the hardware is hung). Other device specific stuff like workarounds or dealing with hardware specific quirks or similar.
6. The creation, initialization, and registration of a struct net_device_ops structure. This structure contains function pointers to the various functions needed for opening the device, sending data to the network, setting the MAC address, and more.
7. The creation, initialization, and registration of a high level struct net_device which represents a network device.
The following code from the igb_probe function and cp_init_one function does some basic PCI configuration.
err = pci_enable_device_mem(pdev); err = dma_set_mask_and_coherent(&pdev->dev, DMA_BIT_MASK(64)); err = pci_request_selected_regions(pdev, pci_select_bars(pdev, IORESOURCE_MEM), igb_driver_name); pci_enable_pcie_error_reporting(pdev); pci_set_master(pdev); pci_save_state(pdev); | rc = pci_enable_device(pdev); rc = pci_set_mwi(pdev); rc = pci_request_regions(pdev, DRV_NAME); pciaddr = pci_resource_start(pdev, 1); rc =pci_resource_len(pdev, 1); regs = ioremap(pciaddr, CP_REGS_SIZE); pci_set_drvdata(pdev, dev); pci_set_master(pdev);

## Slide 8
First, the device is initialized with pci_enable_device_mem. This will wake up the device if it is suspended, enable memory resources, and more. Next, the DMA mask will be set. This device can read and write to 64bit memory addresses, so dma_set_mask_and_coherent is called with DMA_BIT_MASK(64).
Memory regions will be reserved with a call to pci_request_selected_regions, PCI Express Advanced Error Reporting is enabled (if the PCI AER driver is loaded), DMA is enabled with a call to pci_set_master, and the PCI configuration space is saved with a call to pci_save_state.
On the other hand platform bus based drivers allocate registger space using below command
/* Map device registers */ lp->regs = devm_platform_get_and_ioremap_resource(pdev, 0, &ethres); if (IS_ERR(lp->regs)) { ret = PTR_ERR(lp->regs); goto cleanup_clk; }
Network device initialization
The igb_probe/cp_init_one/axienet_probe function does some important network device initialization. In addition to the PCI specific work, it will do more general networking and network device work:
-> The struct net_device_ops is registered.
-> ethtool operations are registered.
-> The default MAC address is obtained from the NIC.
-> net_device feature flags are set.
The struct net_device_ops contains function pointers to lots of important operations that the network subsystem needs to control the device. We’ll be mentioning this structure many times throughout the rest of this post.

## Slide 9
net_device_ops structure
static const struct net_device_ops axienet_netdev_ops = { .ndo_open = axienet_open, .ndo_stop = axienet_stop, .ndo_start_xmit = axienet_start_xmit, .ndo_get_stats64 = axienet_get_stats64, .ndo_change_mtu = axienet_change_mtu, .ndo_set_mac_address = netdev_set_mac_address, .ndo_validate_addr = eth_validate_addr, .ndo_eth_ioctl = axienet_ioctl, .ndo_set_rx_mode = axienet_set_multicast_list, #ifdef CONFIG_NET_POLL_CONTROLLER .ndo_poll_controller = axienet_poll_controller, #endif }; static const struct net_device_ops cp_netdev_ops = { .ndo_open = cp_open, .ndo_stop = cp_close, .ndo_validate_addr = eth_validate_addr, .ndo_set_mac_address = cp_set_mac_address, .ndo_set_rx_mode = cp_set_rx_mode, .ndo_get_stats = cp_get_stats, .ndo_eth_ioctl = cp_ioctl, .ndo_start_xmit = cp_start_xmit, .ndo_tx_timeout = cp_tx_timeout, .ndo_set_features = cp_set_features, .ndo_change_mtu = cp_change_mtu, .ndo_features_check = cp_features_check, #ifdef CONFIG_NET_POLL_CONTROLLER .ndo_poll_controller = cp_poll_controller, #endif }; | static const struct net_device_ops igb_netdev_ops = { .ndo_open = igb_open, .ndo_stop = igb_close, .ndo_start_xmit = igb_xmit_frame, .ndo_get_stats64 = igb_get_stats64, .ndo_set_rx_mode = igb_set_rx_mode, .ndo_set_mac_address = igb_set_mac, .ndo_change_mtu = igb_change_mtu, .ndo_eth_ioctl = igb_ioctl, .ndo_tx_timeout = igb_tx_timeout, .ndo_validate_addr = eth_validate_addr, .ndo_vlan_rx_add_vid = igb_vlan_rx_add_vid, .ndo_vlan_rx_kill_vid = igb_vlan_rx_kill_vid, .ndo_set_vf_mac = igb_ndo_set_vf_mac, .ndo_set_vf_vlan = igb_ndo_set_vf_vlan, .ndo_set_vf_rate = igb_ndo_set_vf_bw, .ndo_set_vf_spoofchk = igb_ndo_set_vf_spoofchk, .ndo_set_vf_trust = igb_ndo_set_vf_trust, .ndo_get_vf_config = igb_ndo_get_vf_config, .ndo_fix_features = igb_fix_features, .ndo_set_features = igb_set_features, .ndo_fdb_add = igb_ndo_fdb_add, .ndo_features_check = igb_features_check, .ndo_setup_tc = igb_setup_tc, .ndo_bpf = igb_xdp, .ndo_xdp_xmit = igb_xdp_xmit, };

## Slide 10
ethtool_ops
netdev->ethtool_ops = &igb_ethtool_ops; static const struct ethtool_ops igb_ethtool_ops = { .supported_coalesce_params = ETHTOOL_COALESCE_USECS, .get_drvinfo = igb_get_drvinfo, .get_regs_len = igb_get_regs_len, .get_regs = igb_get_regs, .get_wol = igb_get_wol, .set_wol = igb_set_wol, .get_msglevel = igb_get_msglevel, .set_msglevel = igb_set_msglevel, .nway_reset = igb_nway_reset, .get_link = igb_get_link, .get_eeprom_len = igb_get_eeprom_len, .get_eeprom = igb_get_eeprom, .set_eeprom = igb_set_eeprom, .get_ringparam = igb_get_ringparam, .set_ringparam = igb_set_ringparam, .get_pauseparam = igb_get_pauseparam, .set_pauseparam = igb_set_pauseparam, .self_test = igb_diag_test, .get_strings = igb_get_strings, .set_phys_id = igb_set_phys_id, .get_sset_count = igb_get_sset_count, .get_ethtool_stats = igb_get_ethtool_stats, .get_coalesce = igb_get_coalesce, .set_coalesce = igb_set_coalesce, .get_ts_info = igb_get_ts_info, .get_rxnfc = igb_get_rxnfc, .set_rxnfc = igb_set_rxnfc, .get_eee = igb_get_eee, .set_eee = igb_set_eee, .get_module_info = igb_get_module_info, .get_module_eeprom = igb_get_module_eeprom, .get_rxfh_indir_size = igb_get_rxfh_indir_size, .get_rxfh = igb_get_rxfh, .set_rxfh = igb_set_rxfh, .get_channels = igb_get_channels, .set_channels = igb_set_channels, .get_priv_flags = igb_get_priv_flags, .set_priv_flags = igb_set_priv_flags, .begin = igb_ethtool_begin, .complete = igb_ethtool_complete, .get_link_ksettings = igb_get_link_ksettings, .set_link_ksettings = igb_set_link_ksettings, }; | dev->ethtool_ops = &cp_ethtool_ops; static const struct ethtool_ops cp_ethtool_ops = { .get_drvinfo = cp_get_drvinfo, .get_regs_len = cp_get_regs_len, .get_sset_count = cp_get_sset_count, .nway_reset = cp_nway_reset, .get_link = ethtool_op_get_link, .get_msglevel = cp_get_msglevel, .set_msglevel = cp_set_msglevel, .get_regs = cp_get_regs, .get_wol = cp_get_wol, .set_wol = cp_set_wol, .get_strings = cp_get_strings, .get_ethtool_stats = cp_get_ethtool_stats, .get_eeprom_len = cp_get_eeprom_len, .get_eeprom = cp_get_eeprom, .set_eeprom = cp_set_eeprom, .get_ringparam = cp_get_ringparam, .get_link_ksettings = cp_get_link_ksettings, .set_link_ksettings = cp_set_link_ksettings, }; | ndev->ethtool_ops = &axienet_ethtool_ops; static const struct ethtool_ops axienet_ethtool_ops = { .supported_coalesce_params = ETHTOOL_COALESCE_MAX_FRAMES ¦ ETHTOOL_COALESCE_USECS, .get_drvinfo = axienet_ethtools_get_drvinfo, .get_regs_len = axienet_ethtools_get_regs_len, .get_regs = axienet_ethtools_get_regs, .get_link = ethtool_op_get_link, .get_ringparam = axienet_ethtools_get_ringparam, .set_ringparam = axienet_ethtools_set_ringparam, .get_pauseparam = axienet_ethtools_get_pauseparam, .set_pauseparam = axienet_ethtools_set_pauseparam, .get_coalesce = axienet_ethtools_get_coalesce, .set_coalesce = axienet_ethtools_set_coalesce, .get_link_ksettings = axienet_ethtools_get_link_ksettings, .set_link_ksettings = axienet_ethtools_set_link_ksettings, .nway_reset = axienet_ethtools_nway_reset, };

## Slide 11
IRQ’s
When a data frame is written to RAM via DMA, how does the NIC tell the rest of the system that data is ready to be processed?
Traditionally, a NIC would generate an interrupt request (IRQ) indicating data had arrived. There are three common types of IRQs: MSI-X, MSI, and legacy IRQs. These will be touched upon shortly. A device generating an IRQ when data has been written to RAM via DMA is simple enough, but if large numbers of data frames arrive this can lead to a large number of IRQs being generated. The more IRQs that are generated, the less CPU time is available for higher level tasks like user processes. The New Api (NAPI) was created as a mechanism for reducing the number of IRQs generated by network devices on packet arrival. While NAPI reduces the number of IRQs, it cannot eliminate them completely.
NAPI allows a device driver to register a poll function that the NAPI subsystem will call to harvest data frames.
1. The intended use of NAPI in network device drivers is as follows:
2. NAPI is enabled by the driver, but is in the off position initially.
3. A packet arrives and is DMA to memory by the NIC.
4. An IRQ is generated by the NIC which triggers the IRQ handler in the driver.
5. The driver wakes up the NAPI subsystem using a softirq. This will begin harvesting packets by calling the drivers registered poll function in a separate thread of execution.
6. The driver should disable further IRQs from the NIC. This is done to allow the NAPI subsystem to process packets without interruption from the device.
Once there is no more work to do, the NAPI subsystem is disabled and IRQs from the device are re-enabled.The process starts back at step 2.
The device driver implements a poll function and registers it with NAPI by calling netif_napi_add. When registering a NAPI poll function with netif_napi_add, the driver will also specify the weight. Most of the drivers hardcode a value of 64. Typically, drivers register their NAPI poll functions during driver initialization.
netif_napi_add(ndev, &lp->napi_rx, axienet_rx_poll);
netif_napi_add(ndev, &lp->napi_tx, axienet_tx_poll);
netif_napi_add_weight(dev, &cp->napi, cp_rx_poll, 16);
netif_napi_add(adapter->netdev, &q_vector->napi, igb_poll);

## Slide 12
The function igb_poll with the NAPI subsystem. It provides a reference to the struct napi_struct associated with this newly created RX queue (&q_vector->napi above). This will be passed into igb_poll when called by the NAPI subsystem when it comes time to harvest packets from this RX queue.
The net_device_ops structure we saw earlier which registered a set of functions for bringing the network device up, transmitting packets, setting the MAC address, etc. When a network device is brought up (for example, with ifconfig eth0 up), the function attached to the ndo_open field of the net_device_ops structure is called. The ndo_open function will typically do things like:
1. Allocate RX and TX queue memory
2. Enable NAPI
3. Register an interrupt handler
4. Enable hardware interrupts
Enabling NAPI is relatively straight forward. A call to napi_enable will flip a bit in the struct napi_struct to indicate that it is now enabled. As mentioned above, while NAPI will be enabled it will be in the off position.
napi_enable(&lp->napi_rx);
napi_enable(&lp->napi_tx);
napi_enable(&cp->napi);
The softirq system in the Linux kernel is a mechanism for executing code outside of the context of an interrupt handler implemented in a driver. This system is important because hardware interrupts may be disabled during all or part of the execution of an interrupt handler. The longer interrupts are disabled, the greater chance that events may be missed. So, it is important to defer any long running actions outside of the interrupt handler so that it can complete as quickly as possible and re-enable interrupts from the device.
The softirq system can be imagined as a series of kernel threads (one per CPU) that run handler functions which have been registered for different softirq events. If you’ve ever looked at top and seen ksoftirqd/0 in the list of kernel threads, you were looking at the softirq kernel thread running on CPU 0.

## Slide 13
static irqreturn_t cp_interrupt (int irq, void *dev_instance) { if (napi_schedule_prep(&cp->napi)) { cpw16_f(IntrMask, cp_norx_intr_mask); __napi_schedule(&cp->napi); } } | static irqreturn_t igb_msix_ring(int irq, void *data) { struct igb_q_vector *q_vector = data; /* Write the ITR value calculated from the previous interrupt. */ igb_write_itr(q_vector); napi_schedule(&q_vector->napi); return IRQ_HANDLED; }
root@rama-Inspiron-3501:/home/rama# cat /proc/net/dev
Inter-| Receive | Transmit
face |bytes packets errs drop fifo frame compressed multicast|bytes packets errs drop fifo colls carrier compressed
lo: 78648 861 0 0 0 0 0 0 78648 861 0 0 0 0 0 0
enp1s0: 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
wlp2s0: 19579109 17479 0 0 0 0 0 0 1601701 6250 0 0 0 0 0 0
docker0: 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
root@rama-Inspiron-3501:/home/rama# cat /proc/softirqs
CPU0 CPU1 CPU2 CPU3
HI: 4034 9380 39306 7424
TIMER: 28734 35230 57754 32040
NET_TX: 1 0 6 3
NET_RX: 283 21893 26053 347
BLOCK: 1805 2099 2856 2292
IRQ_POLL: 0 0 0 0
TASKLET: 39 78 62 314
SCHED: 77103 89026 104056 74772
HRTIMER: 0 0 0 0
RCU: 63961 68038 69233 63023
root@rama-Inspiron-3501:/home/rama#