## Slide 1
Introduction to Embedded Linux
Birth of free software:
1983, Richard Stallman, GNU project and the free software concept. Beginning of the development of gcc, gdb, glibc and other important tools
1991, Linus Torvalds, Linux kernel project, a Unix-like operating system kernel. Together with GNU software and many other open-source components: a completely free operating system, GNU/Linux
1995, Linux is more and more popular on server systems
2000, Linux is more and more popular on embedded systems
2008, Linux is more and more popular on mobile devices
2010, Linux is more and more popular on phones
Embedded Linux is the usage of the Linux kernel and various open-source components in embedded systems

## Slide 2
https://www.youtube.com/watch?v=0_GfMcBmbCg&t=111s

## Slide 3
Embedded Linux Hardware
The Linux kernel and most other architecture-dependent components support a wide range of 32 and 64 bit architectures
▶ x86 and x86-64, as found on PC platforms, but also embedded systems
(multimedia, industrial)
▶ ARM, with hundreds of different System on Chips
(SoC: CPU + on-chip devices, for all sorts of products)
▶ RISC-V, the rising architecture with a free instruction set
(from high-end cloud computing to the smallest embedded systems)
▶ PowerPC (mainly real-time, industrial applications)
▶ MIPS (mainly networking applications)
▶ Microblaze (Xilinx), Nios II (Altera): soft cores on FPGAs
▶ Others: ARC, m68k, Xtensa, SuperH..
▶ Both MMU and no-MMU architectures are supported, even though no-MMU architectures have a few limitations.
▶ Linux does not support small microcontrollers (8 or 16 bit)
▶ Besides the toolchain, the bootloader and the kernel, all other components are generally architecture-independent

## Slide 4
RAM: a very basic Linux system can work within 8 MB of RAM, but a more realistic system will usually require at least 32 MB of RAM. Depends on the type and size of applications.
▶ Storage: a very basic Linux system can work within 4 MB of storage, but usually
more is needed.
• Block storage: SD/MMC/eMMC, USB mass storage, SATA, etc,
• Raw flash storage is supported too, both NAND and NOR flash, with specific
filesystems
▶ Not necessarily interesting to be too restrictive on the amount of RAM/storage: having flexibility at this level allows to increase performance and re-use as many existing components as possible.
▶ The Linux kernel has support for many common communication buses
• I2C
• SPI
• 1-wire
• SDIO
• PCI
• USB
• CAN (mainly used in automotive)
▶ And also extensive networking support
• Ethernet, Wifi, Bluetooth, CAN, etc.
• IPv4, IPv6, TCP, UDP, SCTP, DCCP, etc.
• Firewalling, advanced routing, multicast

## Slide 5
Embedded software development process
Embedded Linux System Architecture:
When doing embedded development, there is always a split between
The host, the development workstation, which is typically a powerful PC
The target, which is the embedded system under development
They are connected by various means: almost always a serial line for debugging purposes, frequently an Ethernet connection, sometimes a JTAG interface for low-level debugging

## Slide 6
▶ Cross-compilation toolchain
• Compiler that runs on the development machine, but generates code for the target
▶ Bootloader
• Started by the hardware, responsible for basic initialization, loading and executing the kernel
▶ Linux Kernel
• Contains the process and memory management, network stack, device drivers and provides services to user space applications
▶ C library
• Of course, a library of C functions
• Also the interface between the kernel and the user space applications
▶ Libraries and applications
• Third-party or in-house
Two ways to switch to embedded Linux
• Use solutions provided and supported by vendors like MontaVista, Wind River or TimeSys. These solutions come with their own development tools and environment. They use a mix of open-source components and proprietary tools.
• Use community solutions. They are completely open, supported by the community

## Slide 7
Embedded Linux Hardware
x86
  Introduced by Intel in 1985
  Large amounts of documentation available
  Most widely used and tested on Linux platforms
  Many applications developed on the x86 for the purpose of porting to other hardware.

## Slide 8
Embedded Linux Hardware
ARM (Advanced RISC Machine)
  No particular manufacturer, maintained by ARM Holdings Ltd.
  ARM Holdings designs CPU cores and the ARM instruction set
  Customers find their own manufacturer which allows for greater customization
  Linux supports ten different ARM CPUs on sixteen different platforms, along with two hundred related boards.

## Slide 9
Embedded Linux Hardware
Busses and Interfaces
  PCI
  PCMCIA
  Parallel Port
  SCSI
  USB
  FireWire
  Serial Port
Linux also supports a wide variety IO devices
  Printers
  Mice
  Sound
  Storage
  Display Devices
The Linux kernel has support for many common communication buses
I2C, SPI, CAN, 1-wire, SDIO, USB and also extensive networking support Ethernet, Wi, Bluetooth, CAN, etc

## Slide 10
ARM introduction
ARM is a family of instruction set architectures for computer processors based on a reduced instruction set computing (RISC) architecture developed by British company ARM Holdings.
A RISC-based computer design approach means ARM processors require significantly fewer transistors than typical processors in average computers. This approach reduces costs, heat and power use. These are desirable traits for light, portable, battery-powered devices—including smartphones, laptops, tablet and notepad computers), and other embedded systems.
A simpler design facilitates more efficient multi-core CPUs and higher core counts at lower cost, providing higher processing power and improved energy efficiency for servers and supercomputers.
ARM Holdings develops the instruction set and architecture for ARM-based products, but does not manufacture products. The company periodically releases updates to its cores. Current cores from ARM Holdings support a 32-bit address space and 32-bit arithmetic; the recently introduced ARMv8-A architecture adds support for a 64-bit address space and 64-bit arithmetic
A architecture adds support for a 64-bit address space and 64-bit arithmetic.
ARM Holdings licenses the chip designs and the ARM instruction set architectures to third-parties, who design their own products that implement one of those architectures—including systems-on-chips (SoC) that incorporate memory, interfaces, radios, etc.
Apple first implemented the ARMv8-A architecture in the Apple A7 chip in the iPhone 5S.

## Slide 11
List of applications of ARM cores

## Slide 12
ARM embedded boards
Beagle Board & Raspberry PI

## Slide 13
Parts of Beagle Board

## Slide 14
Hardware Components
DC Power is the main DC input that accepts 5V power.
Power Button alerts the processor to initiate the power down sequence.
10/100 Ethernet is the connection to the LAN.
Serial Debug is the serial debug port.
USB Client is a miniUSB connection to a PC that can also power the board.
BOOT switch can be used to force a boot from the microSD card if the power is cycled on the board, removing power and reapplying the power to the board..

## Slide 15
Hardware Components
There are four blue LEDS that can be used by the user.
Reset Button allows the user to reset the processor.
microSD slot is where a microSD card can be installed.
microHDMI connector is where the display is connected to.
USB Host can be connected different USB interfaces such as Wi-Fi, BT, Keyboard, etc.

## Slide 16
Key Components

## Slide 17
Key Components
Sitara AM3359AZCZ100 is the processor for the board.
Micron 512MB DDR3L is the Dual Data Rate RAM memory.
TPS65217C PMIC provides the power rails to the various components on the board.
SMSC Ethernet PHY is the physical interface to the network.
Micron eMMC is an onboard MMC chip that holds up to 2GB of data.
HDMI Framer provides control for an HDMI or DVI-D display with an adapter.

## Slide 18
BeagleBone Black block diagram

## Slide 19
• BeagleBoard.org designs have a common philosophy:
• Bring your own peripherals
• Entry level cost
• ARM Cortex-A8 (superscalar)
• Graphics (and possibly DSP) accelerated
• Linux and open source community
• Environment for innovators

## Slide 20
Processor Features
Operating Systems : Linux, Android, Windows Embedded CE
Standby Power : 7mW
ARM CPU : 1 ARM Cortex-A8
ARM MHz(Max) : 275,500,600,800
ARM MIPS : 1000,1200,2000
On-Chip L1 Cache : 64KB
On-Chip L2 Cache : 256KB
General Purpose Memory : 1 16-bit (GPMC,NAND flash, NOR flash)
USB : 2
MMC/SD : 3
CAN : 2
UART (SCI) : 6
ADC : 8-ch 12-bit
PWM(ch) : 3
DMA(ch) : 64- Ch EDMA

## Slide 21
Boot Modes
• eMMC Boot…This is the default boot mode and will allow for the fastest boot
time and will enable the board to boot out of the box without having to purchase
an SD card or an SD card writer.
• SD Boot…This mode will boot from the uSD slot. This mode can be used to
override what is on the eMMC device and can be used to program the eMMC
when used in the manufacturing process or for filed updates.
• Serial Boot…This mode will use the serial port to allow downloading of the
software direct. A separate serial cable is required to use this port.
• USB Boot…This mode supports booting over the USB port.

## Slide 22
Connecting Up Your BeagleBone
Tethered to a PC and

## Slide 23
Connect the Cable to the Board
1. Connect the small connector on the USB cable to the board as shown in Figure
The connector is on the bottom side of the board.

## Slide 24
2. Connect the large connector of the USB
cable to your PC or laptop USB port.
3. The board will power on and the power LED
will be on as shown in Figure below.
Notes: 24

## Slide 25
What is a Raspberry Pi?
Raspberry Pi is the name of a series of single-board computers made by theÂ Raspberry Pi Foundation, a UK charity that aims to educate people in computing and
create easier access to computing education.
The Raspberry Pi launched in 2012, and there have been several iterations and variations released since then. The original Pi had a single-core 700MHz CPU and just 256MB RAM, and the latest model has a quad-core CPU clocking in at over 1.5GHz, and 4GB RAM. The price point for Raspberry Pi has always been under $100 (usually around $35 USD), most notably the Pi Zero, which costs just $5.
Pi 1 Model B (2012)
Pi 1 Model A (2013)
Pi 1 Model B+ (2014)
Pi 1 Model A+ (2014)
Pi 2 Model B (2015)
Pi Zero (2015)
Pi 3 Model B (2016)
Pi Zero W (2017)
Pi 3 Model B+ (2018)
Pi 3 Model A+ (2019)
Pi 4 Model A (2019)
Pi 4 Model B (2020)
Pi 400 (2021)
Pi Model B(2023)
https://www.youtube.com/watch?v=LSJys4vCfJE&t=305s

## Slide 29
Development Tools and Environments
Cross-compilation tool chain
Compiler that runs on the development machine, but generates code
for the target
Boot loader
Started by the hardware, responsible for basic initialization, loading and executing the kernel
Linux Kernel
Contains the process and memory management, network stack,
device drivers and provides services to user space applications
C library
The interface between the kernel and the user space applications
Libraries and applications
Third-party or in-house

## Slide 30
Cross compilation Tool chain:
To build tool chain from scratch
http://www.ifp.illinois.edu/~nakazato/tips/xgcc.html
On Ubuntu:
sudo apt-get update sudo apt-get install crossbuild-essential-armhf
To compile program:
arm-linux-gnueabihf-gcc file_name.c -o output
=> Execute simple programs on BBB/RB Pi
The gcc C compiler enables the embedding of assembly instructions in otherwise normal C functions.
Inline Assembly:
Gcc support this: The asm() compiler directive is used to inline assembly code. For example, this inline assembly directive executes the x86 processor’s rdtsc instruction, which returns the value of the timestamp (tsc) register:
unsigned int low, high;
asm volatile("rdtsc" : "=a" (low), "=d" (high));
/* low and high now contain the lower and upper 32-bits of the 64-bit tsc */

## Slide 31
Cross-compiling Linux Kernel

## Slide 32
Booting on embedded platforms: ROM code
Most embedded processors include a ROM code that implements the initial step of the boot process
▶ The ROM code is written by the processor vendor and directly built into the processor
• Cannot be changed or updated
• Its behavior is described in the processor data sheet
▶ Responsible for finding a suitable boot loader, loading it and running it
• From NAND/NOR flash, from USB, from SD card, from eMMC, etc.
• Well defined location/format
▶ Generally runs with the external RAM not initialized, so it can only load the bootloader into an internal SRAM
• Limited size of the boot loader, due to the size of the SRAM
• Forces the boot process to be split in two steps: first stage boot loader (small, runs from SRAM, initializes external DRAM), second stage bootloader (larger, runs from external DRAM)

## Slide 33
Booting on ARM Atmel AT91 Processor

## Slide 34
Booting on ARM TI OMAP Processor
Boot Beagle board/RP Stop
at Uboot prompt

## Slide 35
Two stage booting sequence

## Slide 36
Boot loaders and firmware Trusted firmware
▶ Traditionally, bootloaders are only used during the booting process
Bootloader loads operating system, jumps to it, and is discarded
▶ Modern SoCs have advanced security mechanisms that require running some sort of trusted firmware
▶ This firmware is loaded by the bootloader, or part of the boot chain itself
▶ This trusted firmware stays resident after control has been passed to the OS
• It is stored in a dedicated portion of the DDR, or some specific SRAM, inaccessible
from the OS
• It provides services to the OS, which the OS cannot perform directly
• Can also be responsible for running a secure OS alongside the regular OS (Linux in
our case)
Modern ARMv7 and ARMv8 processors have
• 4 privilege levels (Exception Levels)
EL3, the most privileged, runs secure firmware
EL2, typically used by hypervisors, for virtualization
EL1, used to run the Linux kernel
EL0, used to run Linux user-space applications
• 2 worlds
Normal world, used to run a general purpose OS, like Linux
Secure world, to run a separate, isolated, secure operating system and applications.
Also called TrustZone by ARM.
▶ EL3 only exists in the secure world
▶ EL2 exists in both secure and normal worlds since ARMv8.4, before that EL2 was
only in the normal world
▶ EL1 and EL0 exist in both secure and normal worlds

## Slide 37
Interfaces with secure firmware
▶ Standardized by ARM
▶ Services
• implemented by the secure firmware
• called by the operating system
▶ Prevents the operating system running in normal world from directly accessing critical hardware resources
▶ PSCI, Power State Coordination Interface
• Power management related: turn CPUs on/off, CPU idle state, platform shutdown/reset
▶ SCMI, System Control and Management Interface
• Power domain, clocks, sensor, performance
▶ Secure firmware implementing these interfaces is
• Mandatory to run Linux on ARMv8
• Mandatory to run Linux on some ARMv7 platforms, but not all
TF-A
▶ Trusted Firmware-A (TF-A) provides a reference implementation of secure world software for Armv7-A and Armv8-A, including a Secure Monitor executing at Exception Level 3 (EL3)
▶ Formerly known as ATF, for ARM Trusted Firmware
▶ Implements the various standard interfaces that operating systems need from the secure firmware
▶ Has drivers for the hardware blocks that are not accessed directly by Linux
▶ Needs to be ported for each SoC
▶ Depending on the platform, may also need to be ported per board: DDR initialization
▶ Used on the vast majority of ARMv8 platforms, and on a few recent ARMv7 platform

## Slide 38
ARM exception levels and worlds

## Slide 39
UEFI vs legacy BIOS
When you build your own PC, you need to configure some settings in the motherboard's BIOS (Basic Input/Output System) before installing an operating system. The BIOS is a firmware that controls the hardware components and boot process of your PC.
UEFI (Unified Extensible Firmware Interface) is a newer standard that replaces the legacy BIOS. UEFI offers more features and benefits, such as faster boot times, better security, larger disk support, and graphical user interface. Legacy BIOS is the old mode that uses a 16-bit code and a limited number of options. Some older hardware and software may not be compatible with UEFI, so legacy BIOS is still available as a fallback option
Boot Loaders:
The boot loader is a piece of code responsible for
  Basic hardware initialization
  Loading of an application binary, usually an operating system kernel, from flash storage, from the network, or from another type of non-volatile storage.
  Possibly decompression of the application binary and execution of the application
  It provides a way to upgrade the firmware without requiring access to internal storage. Used to upgrade firmware on devices,fix bugs, add new features or update security patches
  In the event the OS becomes corrupted or fails to start, the boot loader can be used to recover the device
  In some embedded systems, the boot loader can be used to operating system to boot, download new firmware from remote server and recover the device in case of disaster.

## Slide 40
BeagleBone Linux Boot Process with Trusted Firmware-A Secure Boot
This document describes the Linux boot process on BeagleBone-class boards using Trusted Firmware-A (TF-A) with Secure Boot enabled. This applies to newer TI K3-based SoCs such as AM62x, AM64x, and AM65x.
1. Power-On and ROM Code (BL0)
When power is applied, the CPU begins execution from immutable on-chip ROM code. This ROM code forms the
Root of Trust.
• Boot mode selection via boot pins
• Minimal hardware initialization
• Authentication of the first boot image using keys stored in eFuses
• Loading of TF-A BL2 into internal SRAM
2. TF-A BL2 (Secure Boot Loader)
BL2 runs in Secure EL3 and is responsible for initializing DDR memory and maintaining the secure chain of trust.
• Initialize clocks, DDR, and security firewalls
• Authenticate and load BL31 (TF-A runtime)
• Authenticate and load BL32 (OP-TEE, optional)
• Authenticate and load BL33 (U-Boot)
• DTB(FDT blob) DTB is used across all stages.

## Slide 41
3. TF-A BL31 (Secure Monitor TF-A)
BL31 provides the secure monitor runtime and remains resident for the entire system lifetime.
• Runs in EL3
• Handles Secure Monitor Calls (SMCs)
• Provides PSCI services
• Transitions execution to the non-secure world
→ Does not modify DTB
Acts as dispatcher:
→ Passes DTB pointer to
BL32(OP_TEE)
BL33(U-boot)
4. BL32 (OP-TEE OS – Optional)
OP-TEE runs in Secure EL1 and provides trusted execution services.
• Trusted Applications execution
• Secure storage and cryptographic services
• Communication via SMC through BL31
→ OP-TEE Receives DTB pointer from TF-A
Uses DTB for
→ secure memory layout
→ reserved memory regions
→ Device configuration (secure peripherals)

## Slide 42
5. BL33 (U-Boot – Non-Secure)
U-Boot runs in the non-secure world but is cryptographically verified before execution.
• Board-level initialization
• Loading Linux kernel, device tree, and initramfs
• Optional verification of kernel and device tree
• Jumping to the Linux kernel
6. Linux Kernel Boot
The Linux kernel executes in the non-secure world and completes system initialization.
• Kernel initialization and device probing
• Root filesystem mount
• User space startup (systemd/init)
7. Secure Boot Chain of Trust
The secure boot process enforces a strict chain of trust from ROM to Linux.
ROM → BL2 → BL31 → (OP-TEE) → U-Boot → Linux Kernel

## Slide 43
U-Boot
U-Boot is a typical free software project
▶ License: GPLv2 (same as Linux)
▶ Freely available at https://www.denx.de/wiki/U-Boot
▶ Documentation available at
https://u-boot.readthedocs.io/en/latest/
▶ The latest development source code is available in a Git repository: https://gitlab.denx.de/u-boot/u-boot
▶ Development and discussions happen around an open mailing-list
https://lists.denx.de/pipermail/u-boot/
U-Boot configuration
▶ Configuration system based on kconfig from the Linux kernel
▶ The configs/ directory contains configuration files for supported boards or platforms
• There may be a single configuration supporting multiple boards based on the same
processor
• The configuration files defines all relevant options: CPU type, drivers needed,
U-Boot features to compile in
• Examples:
configs/stm32mp15_basic_defconfig
configs/stm32mp15_trusted_defconfig
▶ Note: migration to kconfig is still on-going
• Not all boards have been converted to the new configuration system.
• Many boards still have a combination of configuration settings in include/configs/
header files, and configuration settings in defconfig files

## Slide 44
Device Tree:
Many embedded architectures have a lot of non-discoverable hardware.
Depending on the architecture, such hardware is either described using C code directly within the kernel, or using a special hardware description language in a Device Tree.
ARM, PowerPC, OpenRISC, ARC, Microblaze are examples of architectures using the Device Tree.
IA Device Tree Source, written by kernel developers, is compiled into a binary Device Tree Blob, passed at boot time to the kernel.
There is one different Device Tree for each board/platform supported by the kernel, available in arch/arm/boot/dts/<board>.dtb.
The boot loader must load both the kernel image and the Device Tree Blob in memory before starting the kernel
Run make Copy the final kernel image to the target storage
can be uImage, zImage, vmlinux, bzImage in arch/<arch>/boot
copying the Device Tree Blob might be necessary as well, they are available in
arch/<arch>/boot/dts
The typical boot process is therefore:
1. Load uImage at address X in memory
2. Load <board>.dtb at address Y in memory
3. Start the kernel with bootm X - Y

## Slide 45
Configuring & Building U-BOOT for Beagle Board
Download the latest version of u-boot : git clone git://git.denx.de/u-boot.git
U-Boot must be configured before being compiled
▶ Configuration stored in a .config file
▶ Load a pre-defined configuration
$ make BOARDNAME_defconfig
Where BOARDNAME is the name of a configuration, as visible in the configs/ directory. Example:
▶ You can then run make menuconfig to further customize U-Boot’s configuration.
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- am335x_evm_defconfig
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- menuconfig

## Slide 46
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- DEVICE_TREE=am335x-boneblack
Produces:
• MLO, the SPL, first-stage bootloader. Called MLO (Mmc LOad) as required on TI platforms.
• u-boot.img, full U-Boot, second-stage bootloader
U-Boot has a concept of FIT image
▶ FIT = Flat Image Tree
▶ Container format that allows to bundle multiple images into one
• Multiple kernel images
• Multiple Device Trees
• Multiple initramfs
• Any other image: FPGA bitstream, etc.
▶ Typically useful for secure booting and to ensure binaries don’t overlap in memory.
▶ Interestingly, relies on the Device Tree Compiler
• .its file describes the contents of the image
• Device Tree Compiler compiles it into an .itb
▶ U-Boot can load an .itb image and use its different elements

## Slide 47
/dts-v1/;
/ {
description = "BeagleBone Black FIT Image";
#address-cells = <1>;
images {
kernel {
description = "Linux kernel";
data = /incbin/("zImage");
type = "kernel";
arch = "arm";
os = "linux";
compression = "none";
load = <0x82000000>;
entry = <0x82000000>;
hash {
algo = "sha256";
};
};
fdt {
description = "BBB Device Tree";
data = /incbin/("am335x-boneblack.dtb");
type = "flat_dt";
arch = "arm";
compression = "none";
hash {
algo = "sha256";
};
};
};
configurations {
default = "conf-bbb";
conf-bbb {
kernel = "kernel";
fdt = "fdt";
};
};
};
mkimage -f image.its image.itb
load mmc 0:1 ${loadaddr} /boot/image.itb
bootm ${loadaddr}

## Slide 48
Each board/platform used to have its own U-Boot environment, with custom
variables/commands
▶ Wish to standardize the behavior of bootloaders, including U-Boot
With the sysboot command, will look for a /extlinux/extlinux.conf or /boot/extlinux/extlinux.conf file describing how to boot, and will offer a prompt in the console to choose between available configurations.
DEFAULT linux
TIMEOUT 30
PROMPT 1
MENU TITLE Boot Menu
LABEL linux
MENU LABEL Linux (normal)
LINUX /boot/Image
INITRD /boot/initrd.img
APPEND root=/dev/mmcblk0p2 rw console=ttyS0,115200
LABEL recovery
MENU LABEL Linux (recovery)
LINUX /boot/Image
APPEND root=/dev/mmcblk0p2 rw single
/boot/extlinux/extlinux.conf
Use FIT if you want:
Production-grade boot
Secure boot
OTA updates
Multiple boards from one image
Use extlinux.conf if you want:
Easy debugging
Fast iteration
Human-editable configs

## Slide 49
Uboot Commands:
Help, ping, printenv, setenv, ping, md, mm, reginfo…
TFTP transfer process:
Network transfer from the development workstation and U-Boot on the target takes place through TFTP
Trivial File Transfer Protocol
Somewhat similar to FTP, but without authentication and over UDP
A TFTP server is needed on the development workstation
sudo apt-get install tftpd-hpa
All files in /var/lib/tftpboot are then visible through TFTP
A TFTP client is available in the tftp-hpa package, for testing
A TFTP client is integrated into U-Boot
Configure the ipaddr and serverip environment variables
Use tftp <address> <filename> to load file
-> Go through U-boot source code files (Refer Doc)
-> Go through U-boot compilation for Freescale with Yocoto Environment
(Log into remote machine)

## Slide 50
Cross Compiling Kernel:
Define ARCH and CROSS_COMPILE as environment variables:
export ARCH=arm
export CROSS_COMPILE=arm-linux-guneabi-
(Expecting your Development machine contains arm cross compiler
sudo apt-get install gcc-arm-linux-gnueabi)
2. Now ﬁnd out the path and name of the cross-compiler executable by looking at the contents of the package:
dpkg -L gcc-arm-linux-gnueabi
3. Default configuration files available, per board or per-CPU family
They are stored in arch/<arch>/configs/, and are just minimal .config This is the most common way of configuring a kernel for embedded platforms
To load a default configuration , just run
make acme_defconfig I This will overwrite your existing .config To create your own default configuration make savedefconfig, to create a minimal configuration file
mv defconfig arch/<arch>/configs/myown_defconfig
-> make menuconfig
-> make
Copy the final kernel image to the target storage it can be
uImage, zImage, vmlinux, bzImage in arch/<arch>/boot
Copying the Device Tree Blob might be necessary as well, they are available in arch/<arch>/boot/dts

## Slide 51
The outline steps are as fallows (bootm command)
1. Check the kernel image is in Legacy format, then check Magic, CRC,…
2. Check if the image type if Multi image,
If it is multi image then extract all information based on number of components in multi image. Based on standard multi image header, it will fill the fallowing fields in image structure with the structure variable name bootm_headers_t images;
3. It invokes int do_bootm_linux(int flag, int argc, char * const argv[], bootm_headers_t *images)
4 .static void boot_jump_linux(bootm_headers_t *images)
5 . (*kernel) (kbd, initrd_start, initrd_end, cmd_start, cmd_end, 0, 0);
Multi Component Image:
mkimage -A powerpc -O Linux -T multi -a 0x0000000 -e 0x000000 -n 'Multi image' -d zimage.bin.gz:fsl-image-core-p5040ds-20131215171719.rootfs.ext2.gz:uImage-p5040ds.dtb Multigrain1

## Slide 53
typedef struct image_header {
uint32_t ih_magic; /* Image Header Magic Number */
uint32_t ih_hcrc; /* Image Header CRC Checksum */
uint32_t ih_time; /* Image Creation Timestamp */
uint32_t ih_size; /* Image Data Size */
uint32_t ih_load; /* Data Load Address */
uint32_t ih_ep; /* Entry Point Address */
uint32_t ih_dcrc; /* Image Data CRC Checksum */
uint8_t ih_os; /* Operating System */
uint8_t ih_arch; /* CPU architecture */
uint8_t ih_type; /* Image Type */
uint8_t ih_comp; /* Compression Type */
uint8_t ih_name[IH_NMLEN]; /* Image Name */
} image_header_t;
typedef struct image_info {
ulong start, end; /* start/end of blob */
ulong image_start, image_len; /* start of image within blob, len of image */
ulong load; /* load addr for the image */
uint8_t comp, type, os; /* compression, type of image, os type */
} image_info_t;

## Slide 54
/*
* Legacy and FIT format headers used by do_bootm() and do_bootm_<os>()
* routines.
*/
typedef struct bootm_headers {
/*
* Legacy os image header, if it is a multi component image
* then boot_get_ramdisk() and get_fdt() will attempt to get
* data from second and third component accordingly.
*/
image_header_t *legacy_hdr_os; /* image header pointer */
image_header_t legacy_hdr_os_copy; /* header copy */
ulong legacy_hdr_valid;
#if defined(CONFIG_FIT)
const char *fit_uname_cfg; /* configuration node unit name */
void *fit_hdr_os; /* os FIT image header */
const char *fit_uname_os; /* os subimage node unit name */
int fit_noffset_os; /* os subimage node offset */
void *fit_hdr_rd; /* init ramdisk FIT image header */
const char *fit_uname_rd; /* init ramdisk subimage node unit name */
int fit_noffset_rd; /* init ramdisk subimage node offset */
void *fit_hdr_fdt; /* FDT blob FIT image header */
const char *fit_uname_fdt; /* FDT blob subimage node unit name */
int fit_noffset_fdt;/* FDT blob subimage node offset */
#endif
#ifndef USE_HOSTCC
image_info_t os; /* os image info */
ulong ep; /* entry point of OS */
ulong rd_start, rd_end;/* ramdisk start/end */
#ifdef CONFIG_OF_LIBFDT
char *ft_addr; /* flat dev tree address */
#endif
ulong ft_len; /* length of flat device tree */
ulong initrd_start;
ulong initrd_end;
ulong cmdline_start;
ulong cmdline_end;
bd_t *kbd;
#endif
} bootm_headers_t;